## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 11
+

## Slide 2: Simplification of Boolean Functions

## Slide 3: 3-1 Introduction
Gate-level minimization refers to the design task of finding an optimal gate-level implementation of Boolean functions describing a digital circuit.

## Slide 4: 3-2 The Map Method
The complexity of the digital logic gates
  The complexity of the algebraic expression
Logic minimization
  Algebraic approaches: lack specific rules
  The Karnaugh map
    A simple straight forward procedure
    A pictorial form of a truth table
    Applicable if the # of variables < 7
A diagram made up of squares
  Each square represents one minterm

## Slide 5: Review of Boolean Function
Boolean function
  Sum of minterms
  Sum of products (or product of sum) in the simplest form
  A minimum number of terms
  A minimum number of literals
  The simplified expression may not be unique

## Slide 6: Two-Variable Map
A two-variable map
  Four minterms
  x' = row 0; x = row 1
  y' = column 0; y = column
1
  A truth table in square diagram
Fig. 3.2(a): xy = m3
Fig. 3.2(b): x+y = x'y+xy'
+xy = m1+m2+m3
Figure 3.2 Representation of functions in the map
Figure 3.1 Two-variable Map

## Slide 7: A Three-variable Map
A three-variable map
  Eight minterms
  The Gray code sequence
  Any two adjacent squares in the map differ by only one variable
    Primed in one square and unprimed in the other
    e.g., m5 and m7 can be simplified
    m5+ m7 = xy'z + xyz = xz (y'+y) = xz
Figure 3.3 Three-variable Map

## Slide 8: A Three-variable Map
m0 and m2 (m4 and m6) are adjacent
m0+ m2 = x'y'z' + x'yz' = x'z' (y'+y) = x'z'
m4+ m6 = xy'z' + xyz' = xz' (y'+y) = xz'

## Slide 9: Example 3.1
Example 3.1: simplify the Boolean function F(x, y, z) = (2, 3, 4, 5)
  F(x, y, z) = (2, 3, 4, 5) = x'y + xy'
Figure 3.4 Map for Example 3.1, F(x, y, z) = Σ(2, 3, 4, 5) = x'y + xy'

## Slide 10: Example 3.2
Example 3.2: simplify F(x, y, z) = (3, 4, 6, 7)
  F(x, y, z) = (3, 4, 6, 7) = yz+ xz'
Figure 3.5 Map for Example 3-2; F(x, y, z) = Σ(3, 4, 6, 7) = yz + xz'

## Slide 11: Four adjacent Squares
Consider four adjacent squares
  2, 4, and 8 squares
  m0+m2+m4+m6 = x'y'z'+x'yz'+xy'z'+xyz' = x'z'(y'+y) +xz'(y'+y) = x'z' + xz‘ = z'
  m1+m3+m5+m7 = x'y'z+x'yz+xy'z+xyz =x'z(y'+y) + xz(y'+y) =x'z + xz = z
Figure 3.3 Three-variable Map

## Slide 12: Example 3.3
🞕 Example 3.3: simplify F(x, y, z) = (0, 2, 4, 5, 6)
F(x, y, z) = (0, 2, 4, 5, 6) = z'+ xy'
Figure 3.6 Map for Example 3-3, F(x, y, z) = Σ(0, 2, 4, 5, 6) = z' +xy'

## Slide 13: Example 3.4
Example 3.4: let F = A'C + A'B + AB'C + BC
  Express it in sum of minterms.
  Find the minimal sum of products expression.
Ans:
F(A, B, C)  (1, 2, 3, 5, 7) = C + A'B
Figure 3.7 Map for Example 3.4, A'C + A'B + AB'C + BC = C + A'B

## Slide 14: 3.3 Four-Variable Map
January 1, 2023
The map
  16 minterms
  Combinations of 2, 4, 8, and 16 adjacent squares
Figure 3.8 Four-variable Map

## Slide 15: Example 3.5
Example 3.5: simplify F(w, x, y, z) = (0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
F = y'+w'z'+xz'
Figure 3.9 Map for Example 3-5; F(w, x, y, z) = Σ(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14) = y' + w' z' +xz'

## Slide 16: Example 3.6
Example 3-6: simplify F = ABC + BCD + ABCD + ABC
Figure 3.9 Map for Example 3-6; ABC + BCD + ABCD
+ ABC= BD + BC +ACD

## Slide 17: Prime Implicants
Prime Implicants
  All the minterms are covered.
  Minimize the number of terms.
  A prime implicant: a product term obtained by combining the maximum possible number of adjacent squares (combining all possible maximum numbers of squares).
  Essential P.I.: a minterm is covered by only one prime implicant.
  The essential P.I. must be included.

## Slide 18: Prime Implicants
Consider F(A, B, C, D) = Σ(0, 2, 3, 5, 7, 8, 9, 10, 11, 13, 15)
  The simplified expression may not be unique
  F = BD+B'D'+CD+AD = BD+B'D'+CD+AB'
= BD+B'D'+B'C+AD = BD+B'D'+B'C+AB'
Figure 3.11 Simplification Using Prime Implicants

## Slide 19: 3-5 Product of Sums Simplification
M0 | M1 | M3 | M2
M4 | M5 | M7 | M6
M12 | M13 | M15 | M14
M8 | M9 | M11 | M10
00 01 11 10
AB 00
01
11
10
Approach #1
  Simplified F' in the form of sum of products
  Apply DeMorgan's theorem F = (F')'
  F': sum of products → F: product of sums
Approach #2: duality
  Combinations of maxterms (it was minterms)
  M0M1 = (A+B+C+D)(A+B+C+D') = (A+B+C)+(DD') = A+B+C
CD

## Slide 20: Example 3.8
🞕 Example 3.8: simplify F = (0, 1, 2, 5, 8, 9, 10) into (a) sum-of-products form, and (b) product-of-sums form:
Figure 3.14 Map for Example 3.8, F(A, B, C, D)= (0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D
a) F(A, B, C, D)= (0, 1, 2, 5, 8,
9, 10) = B'D'+B'C'+A'C'D
b) F' = AB+CD+BD'
» Apply DeMorgan's theorem;
F=(A'+B')(C'+D')(B'+D)
» Or think in terms of maxterms

## Slide 21: Example 3.8 (cont.)
Gate implementation of the function of Example 3.8
Figure 3.15 Gate Implementation of the Function of Example 3.8
Product-of sums form
Sum-of products form

## Slide 22: Sum-of-Minterm Procedure
Consider the function defined in Table 3.2.
  In sum-of-minterm:
F ( x, y, z)  (1, 3, 4, 6)
  In sum-of-maxterm:
Taking the complement of F
F ( x, y, z)  (0, 2,5, 7)
F ( x, y, z)  ( x  z)( x  z)

## Slide 23: Sum-of-Minterm Procedure
Consider the function defined in Table 3.2.
  Combine the 1’s:
Combine the 0’s :
F ( x, y, z)  xz  xz
F'( x, y, z)  xz  xz
Figure 3.16 Map for the function of Table 3.2

## Slide 24: 3-6 Don't-Care Conditions
The value of a function is not specified for certain combinations of variables
  BCD; 1010-1111: don't care
The don't-care conditions can be utilized in logic minimization
  Can be implemented as 0 or 1
Example 3.9: simplify F(w, x, y, z) = (1, 3, 7, 11, 15) which has the don't-care conditions d(w, x, y, z) = (0, 2, 5).

## Slide 25: Example 3.9 (cont.)
F = yz + w'x'; F = yz + w'z
F = (0, 1, 2, 3, 7, 11, 15) ; F = (1, 3, 5, 7, 11, 15)
Either expression is acceptable
Figure 3.17 Example with don't-care Conditions