## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 13
+

## Slide 2: Sequential Logic

## Slide 3: Sequential Circuits
+
Asynchronous
Synchronous
Combinational Circuit
Memory Elements
Inputs
Outputs
Combinational Circuit
Flip-flops
Clock
Inputs
Outputs

## Slide 4: Flip-Flops
+
The memory elements used in clocked sequential circuits
are called flip-flops.
These circuits are binary cells capable of storing one bit of information.
A flip-flop circuit has two outputs; one for the normal value and one for the complement value of the bit stored in it.
Binary information can enter a flip-flop in a variety of ways.
A flip-flop circuit can maintain a binary state indefinitely (as long as power is delivered to the circuit) until directed by an input signal to switch states.

## Slide 5: Flip-Flops
+
There are mainly four types of flip-flops:
SR (Set-Reset) Flip-Flop
D (Data) Flip-Flop
T (Toggle) Flip-Flop
JK Flip-Flop

## Slide 6: Latch
+
A latch is an electronic device that changes its output
immediately on the basis of the applied input.
One can use it to store either 0 or 1 at a specified time.
A latch contains two inputs- SET and RESET, and it also has
two outputs. They complement each other.
One can use a latch for storing one bit of data.
It is a memory device- just like the flip-flop.
But it is not synchronous, and it does not work on the edges of the clock like the flip-flop.

## Slide 7: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0
1
0
0
Q = Q0
Initial Value

## Slide 8: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
1
0
0
0
Q = Q0 Q = Q0

## Slide 9: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0
1
1
0
Q = 0
Q = Q
0

## Slide 10: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1
0
1
0
Q = 0
Q = 0
Q = Q
0

## Slide 11: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
0
1
0
1
Q = 0
Q = 1
Q = Q
0

## Slide 12: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1
0
0
1
Q = Q
0
Q = 0
Q = 1
Q = 1

## Slide 13: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
0
1
1
10
Q = 0
Q = Q
0
Q = 1
Q = Q’

## Slide 14: Latches
+
SR Latch
R
S
Q
Q
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
1 1 1 | 0 | 0
0
1
1
10
Q = 0
Q = Q
0
Q = 1
Q = Q’ Q = Q’

## Slide 15: Latches
+
SR Latch
R
S
Q
Q
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change Reset Set Invalid
S
R
Q
Q
S R | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid Set Reset
No change

## Slide 16: Controlled Latches
+
SR Latch with Control Input
C S R | Q
0 x x | Q0
1 0 0 | Q0
1 0 1 | 0
1 1 0 | 1
1 1 1 | Q=Q’
No change No change Reset
Set Invalid
S
R
Q
Q
S
R
C
S
R
Q
Q
S
R
C

## Slide 17: Controlled Latches
+
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change Reset Set
S
R
Q
Q
D
C
C
Timing Diagram
D
Q
t
Output may change

## Slide 18: Controlled Latches
+
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change Reset Set
C
Timing Diagram
D
Q
Output may change
S
R
Q
Q
D
C

## Slide 19: Flip-Flops
+
Controlled latches are level-triggered
C
Flip-Flops are edge-triggered
CLK
Positive Edge
CLK
Negative Edge

## Slide 20: Flip-Flops
+
Master-Slave D Flip-Flop
D Latch
(Master)
C
Q
D Latch
(Slave)
D
C
Q
Q
D D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave

## Slide 21: Flip-Flops
+
JK Flip-Flop
Q
Q

## Slide 22: Flip-Flops
+
T Flip-Flop
T Q
Q

## Slide 23: Flip-Flop Characteristic Tables
+
D Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change Reset Set Toggle
J Q
K Q
T Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change Toggle

## Slide 24: Flip-Flop Characteristic Equations
+
D Q
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
Q
J Q
K Q
T Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T  Q

## Slide 25: Flip-Flop Characteristic Equations
+
Analysis / Derivation
Q
Q
 | J | K | Q(t) | Q(t+1)
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 
 | 0 | 1 | 1 | 
 | 1 | 0 | 0 | 
 | 1 | 0 | 1 | 
 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 
No change

## Slide 26: Flip-Flop Characteristic Equations
+
Analysis / Derivation
J Q
K Q
 | J | K | Q(t) | Q(t+1)
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 0
 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 
 | 1 | 0 | 1 | 
 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 
No change
Reset

## Slide 27: Flip-Flop Characteristic Equations
+
Analysis / Derivation
J Q
K Q
 | J | K | Q(t) | Q(t+1)
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 0
 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 
No change
Reset
Set

## Slide 28: Flip-Flop Characteristic Equations
+
Analysis / Derivation
J Q
K Q
 | J | K | Q(t) | Q(t+1)
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 0
 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 1
 | 1 | 1 | 1 | 0
No change
Reset
Set
Toggle

## Slide 29: Flip-Flop Characteristic Equations
+
Analysis / Derivation
Q
Q
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
K |  |  |  |  |  | 
 | 0 |  | 1 | 0 |  | 0
J | 1 |  | 1 | 0 |  | 1
 |  | Q |  |  |  | 
Q(t+1) = JQ’ + K’Q