## Slide 1: Preparing for Emergency Response
Lecture 10

## Slide 2: Workplace Emergency?
A workplace emergency is an unforeseen situation that threatens your employees, customers, or the public; disrupts or shuts down your operations; or causes physical or environmental damage. Emergencies may be natural or manmade and include the following: Floods, Hurricanes,Tornadoes, Fires, Toxic gas releases, Chemical spills, Radiological accidents, Explosions, Civil disturbances, and Workplace violence resulting in bodily harm and trauma.

## Slide 3: Emergency Action Plan includes
Developing an emergency action plan means you should do a hazard assessment to determine what, if any, physical or chemical hazards in your workplaces could cause an emergency.
If you have more than one worksite, each site should have an emergency action plan.

## Slide 4
A preferred method for reporting fires and other emergencies;
An evacuation policy and procedure;
Emergency escape procedures and route assignments, such as floor plans, workplace maps, and safe or refuge areas;
Names, titles, departments, and telephone numbers of individuals both within and outside your company to contact for additional information or explanation of duties and responsibilities under the emergency plan;
Procedures for employees who remain to perform or shut down critical plant operations, operate fire extinguishers, or perform other essential services that cannot be shut down for every emergency alarm before evacuating; and
Rescue and medical duties for any workers designated to perform them.

## Slide 5: Alerting Employees to Emergency
Emergency plan must include a way to alert employees, including disabled workers, to evacuate or take other action, and how to report emergencies, as required. Among the steps you must take are the following:
Make sure alarms are distinctive and recognized by all employees
Make available an emergency communications system such as a public address system, portable radio unit, or other means to notify employees of the emergency and to contact local law enforcement, the fire department, and others; and
Stipulate that alarms must be able to be heard, seen, or otherwise perceived by everyone in the workplace. You might want to consider providing an auxiliary power supply in the event that electricity is shut off

## Slide 6: Establish evacuation routes and exits
When preparing emergency action plan, designate primary and secondary evacuation routes and exits.
To the extent possible under the conditions, ensure that evacuation routes and emergency exits meet the following conditions:
Clearly marked and well lit;
Wide enough to accommodate the number of evacuating personnel;
Unobstructed and clear of debris at all times; and
Unlikely to expose evacuating personnel to additional hazards.
If you prepare drawings that show evacuation routes and exits, post them prominently for all employees to see.

## Slide 8: Fires

## Slide 9: Fire Tetrahedron
Basic components of a fire are:
  fuel
  source of ignition
  oxygen
  process of combustion
Commonly referred to as the "fire tetrahedron"

## Slide 10: Common Causes of Fires
Faulty electrical equipment
Flammable and combustible materials
Lack of staff training
Lack of resources and equipment in place
Arson

## Slide 11: Types of Fires
Class A
Ordinary combustibles or fibrous material, wood, cloth, paper, cardboard
Class B
flammable or combustible liquids, gases
Class C
energized electrical equipment
Class D
combustible metal

## Slide 13: Important Safety Elements
Alarms
  Smoke
  Carbon Monoxide
Fire extinguishers
Residential Fire Sprinkler Systems

## Slide 14: Smoke Alarms
Breathing smoke can kill you!
  Smoke is toxic.
  If you must escape through smoke, get low and go under the smoke.

## Slide 15: Alarm Placement & Maintenance
Make sure you can hear the alarm in every place in your home.
They should be loud enough to wake you from sleep.
Check them once a month.
Change the batteries once a year.
Replace them every 10 years.

## Slide 16: Carbon monoxide (CO)
Carbon monoxide (CO) is an invisible, odorless, colorless gas. There is no way to detect it without an alarm.
Minnesota law requires carbon monoxide alarms in all homes, within ten feet of all sleeping areas.
Symptoms of CO poisoning mimic flu-like symptoms.
  If you’re feeling symptoms, immediately move to an open window or go outdoors.
High levels of CO can be fatal,
causing death within minutes.

## Slide 17: HOW TO USE A PORTABLE FIRE EXTINGUISHER
Remember the acronym, "P.A.S.S."— P......Pull the Pin. A......Aim the extinguisher nozzle at the base of the flames. S......Squeeze trigger while holding the extinguisher upright. S......Sweep the extinguisher from side to side, covering the area of the fire with the extinguishing agent.
When in doubt, get out!

## Slide 18: Residential Fire Sprinklers
Fire sprinkler systems save lives
and reduce damage to your property.
Only the sprinkler closest to the fire will activate, spraying water directly on the fire.
90% of fires are contained by the operation of just one sprinkler.

## Slide 19
Chemical Spills